V. Epshteyn,  P. Shatalov (ITEP) ATLAS-FCAL beam tests 2003 Note 6, 2004-Feb-16

Updates: 2004-Feb-11, 2004-June-22, 2005-Mar-25, with P. Gorbunov (Univ. of Toronto & ITEP)

The analysis status report

1. Introduction

In this note the results published in our previous report [Ref.1] are updated, taking the gain calibration into account.  We refer to [Ref.1] for details of the analysis and term definitions.

2. The gain calibration

In each event, the signals are corrected for gain variations by dividing their reconstructed amplitudes [Ref. 1] by factors norm_h or  norm_m (depending on the gain range used for a given channel). These factors are computed for every individual calorimeter channel. The resulting amplitudes are expressed in "average high gain" units. Two slightly different definitions of these factors are employed in this note:

- Definition 1 (V1):

- Definition 2 (V2):

– same as in V1,

where

;

A(DAC, h{m}) – the amplitude measured in calibration runs for given gain range (high or 	medium, respectively) and the DAC value. See [Ref.2] for further details on the 	calibration data processing;

((DAC  –  the average over the DAC values;

((Ch, FEB  – the global average over channels and FEBs.

For an illustration, Fig. 1 shows distributions of norm_h and norm_m for both definitions.

3. Electrons

The response and the resolution are quoted for a cylinder with the radius r_core = 8 cm. Fig. 2 shows the linearity plot for the 4H position.

Position 4L  ─ Figures 2 and 4. With the gain correction applied, the "anomalies" at 150 and 200 GeV, seen in the earlier analysis [Ref. 1], disappear.  The data seem to be insensitive to the gain correction option (V1 or V2).  The parameters of the fits are listed in Table 1. Table 2 gives the numerical values of the measured response and resolution for the 4L beam position and the definition V2 of the gain correction factors.

Position 4H ─ Figure 3. The same remarks, as for 4H, are applicable.

4. Pions

The gain calibration has no visible effect on the pion data.

References

- V.Epshteyn, P.Shatalov and P.Gorbunov, The analysis status report, ATLAS-FCAL internal Note 4, 2003-10-30, http://cern.ch/atlas-fcaltb/Memos (the "Analysis" section).

- V.Epshteyn, P.Gorbunov, A study of non-linear effects in FCAL pulser calibration data,  ATLAS-FCAL internal Note 5  2004-1-25, http://cern.ch/atlas-fcaltb/Memos (the "Analysis" section).

Figures

Figure 1: Values of the correction coefficients norm_h (a) and norm_m (b), for two definitions V1 and V2, as discussed in the text.

Figure 3:  FCAL1 energy resolution for electrons in position 4L, with r_core=8cm, for the definition V2 of norm_m.  The points are: o ─ calibration off, (  ─ calibration on. The line shows the fit with the function  (P in GeV/c). With the alternative definition V1, the data points and the fit are indistinguishable from V2.

Figure 4: Same as in Fig. 3, for the beam position 4H.

# Footnotes

In this and all other plots, the value 200 GeV (rather than 193.1GeV) is attributed to the beam energy of  "200 GeV" points. ─  PG

# Text boxes

V1

V2

V1

V2

4H: resolution

a, %		b, %((GeV/c,	c, %(GeV/c

no correction		3.73(0.4	22.1(5.7	176(7.7   	 (for P(120GeV/c)

with corr. (V1)	3.79(0.25	22.8(3.9	178(5.7

with corr. (V2)	3.76(0.26	23.1(4.0	177(6.1

4L:  resolution

a, %		b, %((GeV/c,	c, %(GeV/c

no correction         	3.74(0.19 	25.2(1.97 	143(3.6	(for P(100GeV/c)

with corr. (V1)  	3.84(0.08 	23.8(1.18 	146.5(2.2

with corr. (V2)	3.76(0.06 	24.5(0.84 	145.5(1.6

a=(3.76(0.06)%

b=(24.5(0.84)%((GeV/c,

c=(145.5(1.6) )%( GeV/c

a=(3.79(0.25)%

b=(22.8(3.9)%((GeV/c,

c=(178(5.7) )%( GeV/c

electrons, 4L

a=(3.76(0.06)%

b=(24.5(0.84)%((GeV/c,

c=(145(1.6) )%( GeV/c

P, GeV/c

σ(E)/E, %

Table 1: the fit parameters of the linearity and the resolution plots, for electrons at 4L, with and without the gain correction

Table 2: The response and resolution for electrons in the 4L position, measured with the FCAL1 area cut  r_core = 8 cm.

| P, GeV/c | 5 | 10 | 20 | 40 | 60 | 80 | 100 | 150 | 200(193.1) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| response, ADC counts | 51.1 | 110.8 | 228 | 467 | 696 | 932 | 1166 | 1744 | 2273 |
| resolution , % | 34.6 | 16.9 | 9.85 | 6.51 | 5.53 | 4.93 | 4.68 | 4.40 | 4.21 |

Figure 5: The "export" version of Fig. 3.

Figure 2: The linearity plot for electrons, position 4H. The fit parameters: calibration off - , calibration on -

where  R is the response in ADC counts, P – the beam momentum in GeV/c.

electrons, 4L

a=(3.76(0.06)%

b=(24.5(0.84)%((GeV/c,

c=(145(1.6) )%( GeV/c

electrons, 4L

a=(3.76(0.06)%

b=(24.5(0.84)%((GeV/c,

c=(145(1.6) )%( GeV/c

P, GeV/c

P, GeV/c

σ(E)/E, %

σ(E)/E, %

Figure 6: Yet another "export" version of Fig. 3.

4L:  linearity

with corr.  	R (ADC)=	11.76*P(GeV/c) – 8.02(0.52 (all points included)

with corr.	R(ADC)=	11.80*P – 8.99(0.52 		(excluding P=150 GeV/c)

4H:  linearity

no  corr.  		R (ADC)=11.77*P(GeV/c) – 20.52

with correction	R=11.67*P – 19.29